## Slide 1: Workshop
DEFROST team

## Slide 2: General overview of the Tutorial

## Slide 3: Session 1
9:00 am to 9:45 am: Presentation of SOFA & general concepts (presentation)
9:45 am to 10:30 am: First-steps tutorial (practice)

## Slide 4: Session 2
11:00 am to 11:30 am:
Objectives of the tutorial and theoretical concepts (presentation)
11:30 am to 12:00 am:
Modeling with FEM, placement of the servomotors (practice)
12:00 am to 12:30 am:
Deformable-Rigid coupling (presentation & practice)
12:30 am to 1:00 pm:
Contact modeling (presentation & practice)

## Slide 5: Session 3
2:00 pm to 2:30 pm: Interfacing simulation with hardware (practice)
2:30 pm to 3:00 pm: Inverse Kinematic (presentation & practice)
3:00 pm to 3:30 pm: Interfacing simulation to a camera with ROS (demo)
3:30 pm to 4:00 pm:
Closed-loop control (presentation & demo)

## Slide 6: SOFA-FRAMEWORK
www.sofa-framework.org

## Slide 7: Context
SOFA: A shared framework between several research teams
Real-time simulation of physical phenomena but more particularly deformable solid mechanics
Open-source framework (LGPL)
Used to create 2 start-up in France (InSimo and Anatoscope)
Before 2015… Mostly centered on medical simulation
  Simulation of soft-tistsues
  Interactions with medical instruments
  Haptic rendering…

## Slide 8: Context
2015 creation of DEFROST team (Inria, Univ. Lille, CNRS, Centrale Lille)
  Use of SOFA for modeling soft robots in real-time
  Take into account the interactions with the environment
  Create new control methods

## Slide 9: Context
Organization of the code
  SOFA-CORE: public (LGPL licence)
    C++ classes
    Versioning using GIT
    Main functionalities
  Public plugins:
    Python binding (LGPL licence)
    Soft-robot direct modeling (LGPL licence)
    Model order reduction (GPL licence)
    …
  Private plugins (binaries distributed freely today only for research)
    Soft-robot inverse
    Beam Adapter

## Slide 10: Context

## Slide 11: Context
Software architecture
  Compilation using CMake
    de/activate options
    shadow builds (own configs)
    ease the dependency management
  Compatible with Linux / MacOS / Windows

## Slide 12: Main principles of SOFA - A simulation in SOFA -

## Slide 13: Main principles of SOFA :: the graph
Hierarchical representation of simulated objects
  Scene organized as a graph (Directed Acyclic Graph, i.e. generalized hierarchy)
  composed of nodes
  nodes contain components
  components have features (Data)
Data can be connected together

## Slide 14: Main principles of SOFA :: the graph
Hierarchical representation of simulated objects
  Scene organized as a graph (Directed Acyclic Graph, i.e. generalized hierarchy)
  composed of nodes
  nodes contain components
  components have features (Data)
Data can be connected together
Let’s try…

## Slide 15: Main principles of SOFA :: the graph
Scene Graph
  Nodes
  Components
  Data in components

## Slide 16: Main principles of SOFA :: multi-level of abstraction
Multi-model representation
  FEM (mechanics)
  Collision
  Visualization

## Slide 17: Main principles of SOFA :: multi-level of abstraction
Split computation into independent components
  Separate problems
  Improve reusability
Deformable model

## Slide 18: Main principles of SOFA :: multi-level of abstraction
Split computation into independent components
  Separate problems
  Improve reusability
Computation on GPU

## Slide 19: Main principles of SOFA :: multi-level of abstraction
Use of templates for most components
  (+) Facilitates the combination of objects of very different nature
  (+) Allows the use of specific data representation, such as the ones handled by GPUs
  (-) C++ code is complex

## Slide 20: Main principles of SOFA :: multi-level of abstraction
FEM
Spring Mass
Rigid
share/sofa/examples/Demos/chainHybrid

## Slide 21: Main principles of SOFA :: main components
Mechanical Object
Mapping
Solvers
ForceField
Topology
Collision Models
Visual Models

## Slide 22: Main principles of SOFA :: main components
Mechanical Object
  store the state vector (DOF)
  template: any geometry type (rigid, frame, 1d, 2d, 3d, 6d …)
  Importance of its place in the graph !

## Slide 23: Main principles of SOFA :: main components
Mechanical Object
FEM Model
DOFs: positions of nodes (Vec3)
Rigid Model
DOFs: positions and orientation
of gravity center (Rigid)

## Slide 24: Main principles of SOFA :: main components
Mapped Mechanical objects: slave models
  position and velocity imposed by the mapping of a parent MechanicalObject
  force can be applied on slave models and transmitted to the parent

## Slide 25: Main principles of SOFA :: main components
Mapped Mechanical objects: slave models
FEM Model
DOFs: positions of nodes (Vec3)
Rigid Model
DOFs: positions and orientation
of gravity center (Rigid)
Collision Model
Mapped DOFs: positions of points (Vec3)
BarycentricMapping
Collision Model
Mapped DOFs: positions of points (Vec3)
RigidMapping

## Slide 26: Main principles of SOFA :: main components
Mapping
  Allow to transfer the motion (pos, vel) to a « slave » model
  Allow to transfer back to the « parent » model some Forces

## Slide 27: Main principles of SOFA :: main components
Mapping
  Allow to transfer the motion (pos, vel) to a « slave » model
  Allow to transfer back to the « parent » model some Forces
FEM Model
DOFs: positions of nodes (Vec3)
Collision Model
Mapped DOFs: positions of points (Vec3)
BarycentricMapping

## Slide 28: Main principles of SOFA :: main components
Mapping
  Allow to transfer the motion (pos, vel) to a « slave » model
  Allow to transfer back to the « parent » model some Forces
FEM Model
DOFs: positions of nodes (Vec3)
imposed positions and velocities
Collision Model
Mapped DOFs: positions of points (Vec3)
BarycentricMapping

## Slide 29: Main principles of SOFA :: main components
Mapping
  Allow to transfer the motion (pos, vel) to a « slave » model
  Allow to transfer back to the « parent » model some Forces
FEM Model
DOFs: positions of nodes (Vec3)
Collision Model
Mapped DOFs: positions of points (Vec3)
BarycentricMapping
Add forces and constraints

## Slide 30: Main principles of SOFA :: main components
Mapping
  Allow to transfer the motion (pos, vel) to a « slave » model
  Allow to transfer back to the « parent » model some Forces
FEM Model
DOFs: positions of nodes (Vec3)
Visual Model
imposed positions

## Slide 31: Main principles of SOFA :: main components
Solvers
  Time integration (Implicit, Explicit)
  Linear Solver (how to solve the system of equations ?)
  Based on visitors
    Importance of their place in the hierarchical structure
    All non-mapped mechanical objects hierarchically placed under the solver are considered to be DOFs

## Slide 32: Main principles of SOFA :: main components
Case 1: independent solvers
FEM Model
Solver (size 3n)
DOFs: n nodes (Vec3)
Rigid Model
Solver (Size 6)
DOFs: 1 Frame(Rigid)
Collision Model
Mapped DOFs: positions of points (Vec3)
BarycentricMapping
Collision Model
Mapped DOFs: positions of points (Vec3)
RigidMapping
ROOT

## Slide 33: Main principles of SOFA :: main components
Case 2: same solver
FEM Model
DOFs: n nodes (Vec3)
Rigid Model
DOFs: 1 Frame (Rigid)
Collision Model
Mapped DOFs: positions of points (Vec3)
BarycentricMapping
Collision Model
Mapped DOFs: positions of points (Vec3)
RigidMapping
ROOT
Solver (size 3n + 6)

## Slide 34: Main principles of SOFA :: main components
ForceFields
FEM Model
EulerImplicit + CGSolver
MecaObject: nodes (Vec3)
TetrahedronFEMForceField
Spring Model
EulerImplicit + CGSolver
MecaObject: nodes (Vec3)
MeshSpringForceField
FFD Model
EulerImplicit + CGSolver
MecaObject: nodes (Vec3)
RegularGridSpringForceField

## Slide 35: Main principles of SOFA :: main components
ForceFields
  Springs
  Mass
  Internal forces computed by FEM
    Different elements: Tetrahedral, Hexahedral, Beam, ..
    Corotational, Hyperelastic approaches
  Described in an unified way to re-use other components of SOFA, like Mechanical objects and solvers

## Slide 36: Main principles of SOFA :: main components
Topology
  Load a mesh
    geometry (points)
    Connectivity of those points
Edge
Quad
Triangle
Hexahedron
Tetrahedron

## Slide 37: Main principles of SOFA :: main components
Possible different topology for each representation (physics, visual, collision)
Mappings links them

## Slide 38: Main principles of SOFA :: main components
Collision model = geometrical representation supporting collisions
Implemented models
  sphere
  triangle
  point
  line
  oriented bounding box

## Slide 39: Main principles of SOFA :: main components
Collision in 3 steps
  Broad phase = intersection of bounding boxes (pairs)
  Narrow phase = computation of intersection (descending hierarchy)
  Response

## Slide 40: Main principles of SOFA :: main components
Collision in 3 steps
  Broad phase = intersection of bounding boxes (pairs)
  Narrow phase = computation of intersection (descending hierarchy)
  Response
Discret intersection method
Layer depth image
Distance maps

## Slide 41: Main principles of SOFA :: main components
Collision in 3 steps
  Broad phase = intersection of bounding boxes (pairs)
  Narrow phase = computation of intersection (descending hierarchy)
  Response
Penalty methods
Lagrange multiplier constraint

## Slide 42: Main principles of SOFA :: Features
Mechanical models
  Rigid bodies
  Articulated rigid bodies
  Deformable models
    FEM: 6 different models including MJED, Co-Rotational, TLED, in CPU and GPU versions
    Spring-Mass model (CPU + GPU)
    Grid-based deformable model
    Beam model (for vessels, catheters, surgical thread, ...)
    Shell model for hollow structures
    and several others…

## Slide 43: Main principles of SOFA :: Features
Contact response & interactions
  Penalty based approach for contacts : Explicit or Implicit integration
  Constraint based approach for contacts
    Linear Complementarity Constraint (LCP) solvers for contacts, NLCP solvers for friction contacts
    individual optimization for the computation of the contact response (depending of the mechanical model)
  Other type of interaction forces or constraints (attachement, sliding points...)

## Slide 44: Main principles of SOFA :: Features
Solvers
  Different type of ODE Solvers: Explicit and Implicit Euler, Newmark scheme, Runge Kutta...
  Efficient solvers for linear matrix systems : (Preconditioned) conjugate gradient, direct solvers (sparse and band tri-diagonal systems), GPU-based solvers
  Multi-grid solvers for volume deformable objects

## Slide 45: Main principles of SOFA :: Features
Python binding
  on-the-fly modifications: data, object creations
  fast prototyping (w/o C++ skills)
  creation of « controllers » : script that take control of object in the simulation or define new user interactions (keyboard, mouse…)
  Creation of « prefab » (presentation during session 2)

## Slide 46: Main principles of SOFA :: conclusion
High modularity
  Efficiency of the implementation
  Fast prototyping
Hierarchical description of models
  Multimodel simulations using mappings
  wide range of algorithms and solvers
More than a research project…
  750, 000 lines of C++ / open-source / gitHub
  cross-platform: Linux, Mac, Win
  Importance of having a consortium with active support.
  The bigger the community, the better…

## Slide 47: Deformable-rigid coupling
Why composite mechanics ?
Soft robot can be composed of rigid sections (backbones)
Importance of computing the coupling between rigid parts and deformable parts.
Deformable
Rigid
Deformable
Slave nodes

## Slide 48: Deformable-rigid coupling
Hierarchical representation
Slave nodes
Rigid Frame
Slave nodes
Rigid Mapping

## Slide 49: Deformable-rigid coupling
Hierarchical representation
Slave nodes
Rigid Frame
Slave nodes
Rigid Mapping
remaining FEM nodes

## Slide 50: Deformable-rigid coupling
Hierarchical representation
Slave nodes
Rigid Frame
Slave nodes
Rigid Mapping
remaining FEM nodes
FEM computation ?
?

## Slide 51: Deformable-rigid coupling
Hierarchical representation
Multi-Mapping Concept
Slave nodes
Rigid Frame
Slave nodes
Rigid Mapping
remaining FEM nodes
FEM computation
?
SubsetMultiMapping
FEM ForceField

## Slide 52: Deformable-rigid coupling
Hierarchical representation
Multi-Mapping Concept
Slave nodes
Rigid Frame
Slave nodes
Rigid Mapping
remaining FEM nodes
FEM computation
SubsetMultiMapping
FEM ForceField
internal
Forces
internal
Forces
internal
Forces

## Slide 53: Deformable-rigid coupling
Hierarchical representation
Multi-Mapping Concept
Common solver
Slave nodes
1 Rigid Frame
Slave nodes
Rigid Mapping
n remaining FEM nodes
FEM computation
SubsetMultiMapping
FEM ForceField
internal
Forces
internal
Forces
internal
Forces
Solver (size 3n + 6)

## Slide 54: Deformable-rigid coupling
Hierarchical representation
Multi-Mapping Concept
Common solver
Slave nodes
K
K
JT
dq
dx
K
J
K
JT
J
jacobian of the Rigid Mapping
J
Solver (size 3n + 6)
with